Troller Model 34: The "Subtractive Suck" Stabilization Project
The Problem: The 3-Volt "Autopilot" Surge
When a locomotive with an 8-wheel pickup and a high-frequency 0.1µF pure capacitor snubber bridges two energized blocks, the track voltage instantaneously jumps +3V. This surge persists for 3–5 seconds after the bridge is cleared, causing a visible LED brightening and motor speed-up.
The Root Cause: Analog Pulse Interference
The Model 34 uses a "brilliantly stupid" 1979 circuit architecture:
1. The Current Pump: A high-impedance 220KΩ / 220µF momentum node drives the base of a TIP120 Darlington.
2. The Subtractive Suck: A PNP transistor pulls current away from the Darlington’s base 60 times a second, creating 60Hz "notches" for low-speed torque.
3. The Failure: A pure .1µF capacitor in the locomotive acts as a reservoir. When bridging blocks, it shunts the PNP's pulse, "filling in" the notches. The Darlington flips from Pulsed DC to Pure Peak DC (+3V).
4. The Memory: This surge overcharges the 220µF momentum cap. The 3–5 second "slow-down" is the RC decay of that cap bleeding back through the 220KΩ resistor.

The "Stereo-Grade" Solution
1. Locomotive Side: The RC Snubber
- Mod: Convert the pure capacitor to a True RC Network.
- Part: Add a 47Ω 1/4W Flameproof Resistor in series with the .1µF MLCC.
- Result: The resistor "de-tunes" the cap. It still suppresses Athearn Blue Box motor sparks but prevents the cap from "swallowing" the throttle's 60Hz control pulse.
2. Throttle Side: Thermal & Electrical Armor
- Transistor: Re-install the stock-spec TIP120 Darlington.
- Mounting: Ditch the factory clips. Use Mica/Sil-Pad and NTE Thermal Paste; bolt directly to the chassis.
- Flyback Guard: Install a 1N4005 or 1N4007 Diode across the Collector (Cathode) and Emitter (Anode). This "snubs" the motor's inductive kickback (Back-EMF) before it can hit the Darlington.
- Power Rail: Replace the 1A discrete bridge with a 2A Monolith Bridge (Pasted) and upgrade internal filter caps to 35V.

Final Engineering Verification
- Waveform: 60Hz "Suck" notches now survive block-bridging (Verified via Velleman PC Scope).
- Stability: High-frequency "flicker" on dirty track is eliminated by the 1N400x flyback.
- Result: The 3V "Mystery Speedup" is Checkmated.

Github Note: This fix stabilizes the Troller's high-impedance momentum circuit against modern hardwired and snubber-equipped locomotives.